## Slide 1: Lab #B-Convolution Filtering
111061545 陳揚哲

## Slide 2: Outline
Introduction to convolution
Performance requirement of 1080 HD video
Software implementation
Hardware Estimation and Implementation
Performance analysis
Explain what we learn from this lab

## Slide 3: Introduction to convolution
Implement sum-of-product with the matrix
Different filter has different application.
(edge detection, noise filtering, and so on.)
The matrix of Sobel Edge Detection

## Slide 4: Filtering the image
Select the input pixel
Extracting the matrix whose size is same as the filter matrix.
Calculating the sum-of-product with two matrix.
The result is the output pixel value.

## Slide 5: Performance requirement of 1080 HD video
Video resolution(Width * Height)：1920x1080
Frame rate(FPS)：60
Pixel depths(Bits)：8
Color Channels(YUV)：3
Throughputs (Pixel/s, output)：1920 x 1080 x 3 x 60 = 373 MB/s

## Slide 6: Software implementation
There’re 4 for-loops in code.
Outer two loops：
  Define the pixel required to be processed.
Inner two loops：
  Performing sum-of-product calculation.

## Slide 7: Software implementation
We have 3 channel (YUV) for calculation.
Using OpenMP to apply parallel operation.

## Slide 8: Software implementation
To generate 1080 HD video, the throughput need to be 373 MB/s.
Acceleration factor = = = 18.5

## Slide 9: Hardware Estimation
The core compute is done in a 4-level nested loop
Inner two loops are doing the sum-of-product on a coefficient matrix and image.
The matrix sizes are defined by the coefficient matrix, which is 15x15.
The inner two loops are performing a dot product of size 225(15x15).
In other words, the two inner loops perform 225 multiply-accumulate (MAC) operations for every output pixel produced.

## Slide 10: Hardware Estimation - Baseline
Assume performing one MAC per cycle.
We can estimate the hardware performance.
  MAC per cycle：1
  Hardware clock frequency(FMAX)(MHz)：300
  Throughput：300/225 (per output pixel) = 1.33 MB/s
Memory bandwidth requirement.
  Output memory bandwidth = Throughput = 1.33 MB/s
  Input memory bandwidth = Throughput x 225 = 300 MB/s
Acceleration Factor = = = 280

## Slide 11: Hardware Estimation - Optimized
We can unrolled the inner two loop to increase the performance by 225 (generate 1 output pixel per cycle)
Estimate the hardware performance.
  Throughput = FMAX x Pixel produced per cycle = 300 x 1 = 300 MB/s
Memory bandwidth requirement.
  Output memory bandwidth = Throughput = 300 MB/s
  Input memory bandwidth = Throughput x 225 = 300 x 225 = 67.5 GB/s
This input memory bandwidth is too large. Using caching scheme to reduce bandwidth to around 300 MB/s.

## Slide 12: Hardware Estimation – Compute units
To generate 1080 HD video, the throughput need to be 373 MB/s.
Increase the compute units for 3 channel (YUV). Process all data on sperate compute units in parallel.
Throughput estimation
  Throughput = Performance of single compute unit x No. compute units
  = 300x3 = 900 MB/s
  Acceleration against software implementation = = 44.67x
  Kernel latency = = 6.9 ms
  Video processing rate = = 144 FPS

## Slide 13: Hardware implementation - Dataflow
Functions in dataflow
  ReadFromMem: reads pixel data or video input from main memory
  Window2D: local cache with wide(15x15 pixels) access on the output side
  Filter2D: core kernel filtering algorithm
  WriteToMem: writes output data to main memory

## Slide 14: Hardware implementation-Top-level function
#pragma HLS DATAFLOW
  Dataflow process enables task-level pipelining, allowing functions and loops to overlap in their operation

## Slide 15: Hardware implementation – ReadFromMem
Read the data from main memory

## Slide 16: Hardware implementation – Window2D
We build two basic block：”Window” and “line buffer”
  "Window" block holds FILTER_V_SIZE * FILTER_H_SIZE pixels.
  “line buffer” block holds (FILTER_V_SIZE-1) * MAX_IMAGE_WIDTH pixels.

## Slide 17: Hardware implementation – Window2D
“Window” holds the FILTER_V_SIZE * FILTER_H_SIZE pixels
Once we calculate the next pixel, since there’s a large overlap area, only a column moves out from the left, and a column moves in from the right.
From window 10
From line buffer
From ReadFromMem

## Slide 18: Hardware implementation – Window2D
“line buffer” holds (FILTER_V_SIZE-1) * MAX_IMAGE_WIDTH pixels.
In general, it requires FILTER_V_SIZE lines, but a line is reduced.

## Slide 19: Hardware implementation – Window2D
#pragma HLS ARRAY_PARTITION variable=LineBuffer dim=1 complete
  Full partition of LineBuffer
#pragma HLS DEPENDENCE variable=LineBuffer inter false
  LineBuffer has no data dependency between loops
#pragma HLS DEPENDENCE variable=LineBuffer intra false
  LineBuffer has no data dependency in loop

## Slide 20: Hardware implementation – Window2D
#pragma HLS LOOP_TRIPCOUNT max=max_iterations
  Define max iteration for loops, using for analysis
#pragma HLS PIPELINE II=1
  Set II (initiation interval) to be 1

## Slide 21: Hardware implementation – Window2D

## Slide 22: Hardware implementation – Filter 2D
Load filter matrix from ReadFromMem and matrix form Window2D

## Slide 23: Hardware implementation – Filter 2D
#pragma HLS ARRAY_PARTITION variable=coeffs complete dim=0
  Full partition to perform convolution calculation
#pragma HLS PIPELINE II = 1
  Set II (initiation interval) to be 1

## Slide 24: Hardware implementation – WriteToMem
Write output to main memory

## Slide 25: Performance analysis
Find out the throughput = 847 MB/s, closed to estimation 900 MB/s

## Slide 26: Performance analysis – Compute unit

## Slide 27: Performance analysis - data transfer
It can be seen that the host read and write bandwidth is not fully utilized as there are gaps.

## Slide 28: Conclusion
Understand how to build, run, analyze the convolution filter
Estimate performance and compare it with actual performance